## Slide 1: Intelligent Vehicular Accident Prevention System
Supervisor:
Dr Imtiaz Alam
Group Members:
Abdul Qadir Shahbaz 01-133122-001
Muhammad Waqas 01-133122-071

## Slide 2: Agenda
Introduction
Problem Statement
Objectives
Methodology
Components Used
Block Diagram
Interfacing with Arduino
Applications & Benefits
Future Enhancement
Conclusion

## Slide 3: Introduction
To design a system that can sense accidental condition by communicating other vehicle.
This system is capable of generating warning and insure safety by automatically applying brakes in a critical condition.
Convenient and accident free travelling is possible

## Slide 4: Problem Statement
According to WHO 1.2 million people die in road accident every year. Up till now there is no system present which warn you before collision on places like blind spot, suddenly changing lane and on critical distance.

## Slide 5: Objectives
To design a system that
Generate warning on critical distance
Maintain a safe distance
Generate warning on over speeding
Apply auto brakes

## Slide 6: Methodology
Distance
Using distance formula
Communication
Automatic brakes
Automation
V2V
Distance Calculation
Duplex
Least distance and high speed

## Slide 7: Distance Calculation (Approach#01)
Other vehicle should also equipped with same system
Through GPS co-ordinates are read
NRF is used to transmit co-ordinates to other vehicle
Using “Distance formula” distance of both vehicles are calculate

## Slide 8: Distance Calculation (Approach#02)
Stand alone approach
Calculating the distance from sensor values
D1 representing the distance from sensor on LCD

## Slide 9: Communication
Ad-hoc network is responsible for V2V communication
Network is Ad-hoc as it do not rely on pre existing infrastructure
A kind of artificial intelligence that helps vehicles to behave in intelligent manners during vehicle-to-vehicle collisions, accidents
Using NRF Ad-hoc network is established

## Slide 10: Automation
Brakes are applied automatically
PWM interfacing with Arduino
DC motor interfacing with Arduino
Controlling speed of motor

## Slide 12: Components Used
Arduino Mega 2560
GPS Module SKM 53
Ultrasonic Sensor HC-SR04
NRF Sensor 24L01
Modular Robotic Vehicle
LCD 16X4
H-Bridge L298H
PWM
DC Motors
Variable Power Supply
Buzzer

## Slide 13: Block Diagram
Arduino
GPS
NRF
LCD
Power supply
Ultrasonic Sensor

## Slide 14: Interfacing with Arduino MEGA 2560
GPS
NRF sensor
Ultrasonic sensor
LCD
PWM

## Slide 15
GPS coordinates
Safe
Violation
Warning
S<=40 && D>100
START
NO
S<=50||D<=100
S>50||D<40
NO
NO
Auto Brakes
END

## Slide 16
DC 5V,9V
Supply Unit
Control Unit
NRF 24l01
Communication
PWM/
Robotic car
Automation
GPS/
Distance Formula
Distance Measuring

## Slide 17: GPS Coordinates Check on Serial monitor Screen

## Slide 18: Test for NRF
Sender Side

## Slide 19
Receiver Side

## Slide 20: Pulse width Modulation (PWM)
PWM circuit Board
Duty Cycle wave representation

## Slide 21: Implemented Module
Master (Vehicle 01)
Slave (Vehicle 02)

## Slide 22: Applications & Benefits
Reduce the traffic congestion
Less chances of accident etc.

## Slide 23: Future Enhancement
Lane detection
Pedestrian detection
Road signal detection

## Slide 24: Conclusion
V2V communication is implemented successfully. Our vehicle is intelligent enough to generate warning before potential crash. System not depend on driver only as humans have greater tendency of error as compare to machines. Brakes are applied automatically on critical distance a step toward autonomous car.

## Slide 25: Q/A

## Slide 26: Thank You